## Slide 1
CYBERMACS INTERNATIONAL APPLIED CYBERSECURITY CONFERENCE & SUMMER SCHOOL — 2026
L-RAPID
Lightweight Reversible and Privacy-Preserving IIoT Data-Perturbation System
Packed word-parallel obfuscation with exact numerical utility for legacy Modbus telemetry
Authors: Rabbi Hasan Himel, Tayyaba Basri, Hamza Haroon, Aditya Mitra
Supervisors: Assoc. Prof. Dr. E. Fatih Yetkin, Asst. Prof. Dr. Tuğçe Ballı
Department of Management Information Systems | CyberMACS Programme | Kadir Has University, Istanbul, Türkiye

## Slide 2
BACKGROUND & MOTIVATION
Cleartext Telemetry in Legacy Critical Infrastructure
1
A 1979 Protocol, Still Everywhere
Modbus was designed for isolated serial links and still powers over 60% of today’s industrial infrastructure — water treatment, energy grids, factories.
2
Zero Built-In Protection
Register telemetry (FC1–FC4) is transmitted entirely in cleartext, with no authentication and no encryption.
3
Replacement Is Not an Option
Upgrading legacy PLCs costs millions of dollars and requires downtime that plant operators cannot absorb.
4
A Widening Attack Surface
Cloud analytics now pull this cleartext stream over cellular and Wi-Fi links — open to wiretapping, adversarial-ML profiling, and sabotage reconnaissance.
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
2 / 14

## Slide 3
RESEARCH GAP
Why Conventional Defenses Fail on Legacy IIoT
Heavy Cryptography (AES / TLS)
Legacy 8/16-bit PLCs (16–48 MHz) have no AES-NI acceleration.
Software AES-128 costs roughly 10.5 µs per packet — far above sub-millisecond Modbus scan-cycle budgets.
Handshake and buffering overhead exhausts memory on constrained devices.
Verdict: unviable for real-time legacy control loops.
Noise-Based Differential Privacy
Gaussian / Laplacian perturbation permanently distorts the original sensor value.
Cloud anomaly-detection and safety-monitoring systems then act on corrupted inputs.
A 1–2% permanent error on pressure or chlorine level can trigger a false safety shutdown.
Verdict: unacceptable for precision SCADA telemetry.
Central Research Question Can we achieve high-throughput, in-flight telemetry obfuscation on constrained legacy hardware while guaranteeing 100% exact numerical restoration for authorized cloud systems?
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
3 / 14

## Slide 4
SYSTEM ARCHITECTURE
L-RAPID: Three-Tier Reversible Data Perturbation
1 Legacy Edge PLC
Reads Modbus registers FC1–FC4
Packs four 16-bit values into one 64-bit word
Applies packed XOR: C = P ⊕ K
Executes in 0.15 µs per packet
→
2 Untrusted Wiretap Link
Public internet, 4G, or Wi-Fi gateway
Adversary sees only high-entropy values
Static-adversary accuracy: 48.8%
Adaptive-adversary accuracy: 49.9%
→
3 Authorized Cloud Ingestion
Shares synchronization state with the PLC
Re-applies XOR: P = C ⊕ K
100% exact bit-for-bit restoration
Preserves the 98.47% baseline detection accuracy
Self-Inverting Principle: Ciphertext = Plaintext ⊕ Key ⇒ Restored = (Plaintext ⊕ Key) ⊕ Key = Plaintext
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
4 / 14

## Slide 5
CORE TECHNIQUE
Packed 64-Bit Word-Parallel XOR Masking
Four contiguous 16-bit Modbus registers are packed into a single 64-bit word and masked with one packed keystream, instead of masking each register separately.
uint64_t packed = ((uint64_t)FC1 << 48) |
((uint64_t)FC2 << 32) |
((uint64_t)FC3 << 16) |
((uint64_t)FC4);
packed_perturbed = packed ^ keystream_64;
Honest engineering claim: the speedup is architectural word-level parallelism, not cryptographic diffusion — plain XOR does not mix bits across register boundaries; each register stays independently masked by its own 16-bit block.
0.15 µs
Per-packet latency, packed 64-bit XOR — 10× faster than masking each 16-bit register separately (1.48 µs)
2⁶⁴ states
Packed masking domain (≈ 1.84 × 10¹⁹ combinations) per 64-bit packet
Prototype → Production
Static PRNG seed (reproducibility) replaced by ChaCha20 / ASCON-128a with a per-packet nonce in deployment
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
5 / 14

## Slide 6
DATASET & BASELINE
ToN_IoT Modbus Benchmark and Baseline Detection
The Modbus Telemetry Subset
31,106 industrial telemetry samples: 15,000 normal (48%) and 16,106 attack (52%).
Five attack categories: Injection, Backdoor, Scanning, XSS, Password.
Four Modbus function-code registers FC1–FC4, represented as 16-bit unsigned integers (0–65,535).
Low variance ratios (0.56–0.58) show the raw signal is information-rich and hard to model externally.
Baseline Detection Model
Random Forest classifier, 80/20 stratified split (24,884 train / 6,222 test).
Only 16 false positives and 79 false negatives out of 6,222 test samples.
98.47%
binary detection accuracy on raw telemetry
weighted F1: 0.9847
Raw Modbus telemetry has a highly exploitable discriminative structure — directly motivating in-transit obfuscation before transmission.
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
6 / 14

## Slide 7
SECURITY EVALUATION
Dual Threat Modeling: Static vs. Adaptive Adversary
Static Adversary
Distribution shift
Deploys a model pre-trained on clean historical telemetry
Evaluates perturbed traffic directly, without retraining
48.8%
detection accuracy (from 98.47%)
Adaptive Adversary
Active retraining
Has intercepted perturbed traffic and ground-truth labels
Retrains a fresh Random Forest directly on perturbed features (80/20 split)
49.9%
detection accuracy — a coin toss
Key finding: retraining on perturbed data still fails to beat 50% — the suppression is not a covariate-shift artifact, it eliminates the discriminative correlation between features and attack labels.
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
7 / 14

## Slide 8
SECURITY EVALUATION
Empirical Validation: Confusion-Matrix Triad
Figure 1. (A) Clean baseline — 98.47% utility. (B) Adaptive adversary — collapses to the ~50% random-guessing floor. (C) Cloud restoration — recovers 100% exact baseline detection fidelity.
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
8 / 14

## Slide 9
BENCHMARK RESULTS
Computational Latency vs. Standard Cryptography
Perturbation Scheme | Exact Reversibility | Adaptive Adv. Accuracy | Per-Packet Latency | Speedup vs. AES-128-CBC
Gaussian Noise (σ = 0.5) | 100.0% | 50.8% | 1.82 µs | 5.8× faster
Laplacian Noise (b = 0.5) | 100.0% | 49.6% | 2.10 µs | 5.0× faster
XOR 16-bit (register-level) | 100.0% | 50.2% | 1.48 µs | 7.1× faster
XOR 64-bit — packed word (ours) | 100.0% | 49.9% | 0.15 µs | 69.8× faster
ChaCha20 (CSPRNG stream cipher) | 100.0% | 50.0% | 7.12 µs | 1.5× faster
AES-128-CBC (standard block mode) | — | 49.7% | 10.54 µs | 1.0× (reference)
Every reversible method achieved 100% exact-match restoration across all 31,106 samples — zero numerical distortion. Packed XOR-64 is roughly 70× faster than AES-128-CBC and 59× faster than AES-128-CTR.
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
9 / 14

## Slide 10
BIT-DEPTH ANALYSIS
Parametric K-Bit Sweep: Tuning Perturbation Intensity
Chart: XOR Keystream Bit-Depth K (bits perturbed per register)
| K=1 | K=2 | K=3 | K=4 | K=6 | K=8 | K=10 | K=12 | K=14 | K=16
Attacker Detection Accuracy (%) | 98.1 | 98 | 98 | 98 | 98 | 97.8 | 96.4 | 75.9 | 52.6 | 49.6
Random-Guessing Threshold (50%) | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50
K = 1–8 bits
Upper bits stay unperturbed — detection accuracy stays near 98%.
K = 10–12 bits
Accuracy begins collapsing sharply — down to 75.9% at K=12.
K = 14–16 bits
Full privacy collapse: 49.6% at K=16 — all 16 bits must be scrambled for adaptive-AI immunity.
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
10 / 14

## Slide 11
INDUSTRIAL IMPACT
Real-World Deployment: Where This Applies Today
1
Smart Water Treatment
Remote pump and chlorination stations transmit over 4G to regional SCADA.
Noise-based DP is unsafe here — permanent distortion of chlorine or tank levels can trigger false shutdowns.
L-RAPID scrambles telemetry in 0.15 µs and the cloud restores exact values with 100% utility.
2
Renewable Power Substations
Wind and solar sites stream grid frequency and voltage every 10–50 ms.
Software AES causes buffer overflow and desync under such strict latency budgets.
At 0.15 µs, L-RAPID adds effectively zero lag while blocking reconnaissance.
3
Factory Predictive AI
Plants stream vibration and heat telemetry to public cloud AI platforms.
Wiretapped raw streams let competitors infer recipes and production volumes.
The gateway scrambles data pre-ingestion; only authorized engineers reverse it for digital twins.
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
11 / 14

## Slide 12
SECURITY ANALYSIS & FUTURE WORK
Kerckhoffs's Principle and the Production Roadmap
Security Relies on Key Secrecy, Not Obscurity
Publishing the algorithm does not weaken it — as long as the key K stays secret.
Knowing C = P ⊕ K reveals zero bits about the secret keystream — all plaintexts remain equally likely.
A 64-bit packed word spans ≈ 1.84 × 10¹⁹ states; brute-forcing one frame at 1B keys/sec would take over 580 years.
Production keystream derivation is per-packet — knowing packet #1 gives no help decrypting packet #2, defeating known-plaintext attacks.
Production Roadmap
Dynamic keystream: replace the prototype's static seed with ChaCha20 or ASCON-128a paired with a per-packet nonce, for forward secrecy.
Hardware-in-the-loop: deploy on physical Siemens S7-1200 and Schneider Electric Modbus PLCs; profile power and CPU jitter.
Full journal paper: expand this conference abstract with formal mutual-information leakage bounds.
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
12 / 14

## Slide 13
SUMMARY
Conclusion & Contributions
0.15 µs
Sub-Microsecond Speed
~70× faster than AES-CBC
10× faster than 16-bit XOR via packed word parallelism
Zero real-time lag on legacy PLCs
49.9%
Adaptive AI Defense
Baseline detection: 98.47%
Adaptive attacker held at coin-toss accuracy, even after retraining
No exploitable discriminative structure remains
100%
Exact Utility
Exact-match restoration, 0 reconstruction error
No permanent signal distortion, unlike differential privacy
Full fidelity for cloud analytics
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
13 / 14

## Slide 14
Thank You
Questions & Discussion
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation
14 / 14