## Slide 1
CYBERMACS INTERNATIONAL APPLIED CYBERSECURITY CONFERENCE & SUMMER SCHOOL — 2026
L-RAPID: Lightweight Reversible And Privacy-Preserving IIoT Data-Perturbation System
High-Speed Packed Word-Parallel Obfuscation with Exact Numerical Utility for Legacy Modbus Telemetry
Authors: Rabbi Hasan Himel, Tayyaba Basri, Hamza Haroon, Aditya Mitra
Supervisors: Assoc. Prof. Dr. E. Fatih Yetkin, Asst. Prof. Dr. Tuğçe Ballı
Department of Management Information Systems | CyberMACS Programme | Kadir Has University, Istanbul, Türkiye
Supported by the European Union (Erasmus+ CyberMACS, Project #101082683) and TÜBİTAK-1001 (Project #125E288)
Notes: SPEAKER SCRIPT:
Good morning/afternoon distinguished committee members, professors, and fellow researchers. My name is Rabbi Hasan Himel, representing our research team from the Erasmus Mundus Joint Master's Programme in Applied Cybersecurity (CyberMACS) at Kadir Has University.
Today, I am thrilled to present our work titled: 'L-RAPID: Lightweight Reversible And Privacy-Preserving IIoT Data-Perturbation System.' This research tackles a critical dilemma in industrial cybersecurity: how to protect legacy industrial controllers from eavesdropping and adversarial machine learning, without sacrificing sub-millisecond real-time performance or data utility for the cloud.

## Slide 2
BACKGROUND & MOTIVATION
Cleartext Telemetry in Legacy Critical Infrastructure
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 2 of 13
1. The 1979 Industrial Reality
• Standard Protocol: Modbus was designed in 1979 for isolated serial networks.
• Widespread Usage: Still powers >60% of modern industrial infrastructure (water treatment, energy grids, factories).
• Unencrypted Streams: Transmits register telemetry (FC1–FC4) entirely in cleartext with zero authentication.
• High Replacement Cost: Replacing legacy PLCs costs millions and requires catastrophic downtime.
2. The Security Threats
• Wiretapping (MitM): Adversaries intercept telemetry on untrusted cellular, Wi-Fi, or edge links.
• Adversarial ML: Attackers train machine learning classifiers on raw register patterns.
• Corporate Espionage: Competitors deduce production volumes, operational cycles, and secret recipes.
• Targeted Sabotage: Precursor reconnaissance enables Stuxnet-like physical equipment damage.
3. The Operational Requirement
• Cloud Analytics: Modern plants stream telemetry to the cloud for AI digital twins and anomaly detection.
• Precision Sensitivity: Control decisions demand exact floating-point and integer measurements.
• Intolerance to Noise: A 1–2% permanent error in chlorine or pressure triggers safety shutdowns.
• The Core Objective: Scramble telemetry in-transit while guaranteeing 100% exact cloud restoration.
Notes: SPEAKER SCRIPT:
To understand why this problem is urgent, we must look at the reality of modern industry. The Modbus protocol was engineered in 1979—decades before cybersecurity was a concern. Today, it powers over 60% of critical infrastructure, including municipal water distribution, power grid substations, and automotive plants.
Modbus has zero built-in encryption. As factory operators connect legacy PLCs to cloud platforms, adversaries can wiretap network streams and train machine learning models to infer operational states, steal manufacturing intellectual property, or prepare for targeted physical sabotage.
However, factory owners cannot just replace every multi-thousand dollar PLC. We need a solution that works on legacy hardware today without disrupting operational safety.

## Slide 3
RESEARCH GAP
Why Conventional Defenses Fail on Legacy IIoT
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 3 of 13
Limitation of Heavy Cryptography (AES / TLS)
• Hardware Constraint: Legacy 8-bit/16-bit PLCs (16–48 MHz) lack dedicated AES-NI hardware instructions.
• Latency Penalty: Software AES-128 incurs ~10.5 µs per packet—violating sub-millisecond Modbus scan cycles.
• Resource Exhaustion: Handshake overhead and stateful buffering cause memory overflow and dropped packets.
• Practical Verdict: Unviable for real-time legacy industrial control loops.
Limitation of Differential Privacy (Noise Addition)
• Irreversible Distortion: Gaussian or Laplacian perturbation permanently destroys original sensor values.
• Utility Destruction: Cloud anomaly detection algorithms and safety monitoring systems receive corrupted inputs.
• Safety Risks: Permanent noise masks genuine equipment anomalies or triggers false emergency shutdowns.
• Practical Verdict: Unacceptable for safety-critical precision SCADA telemetry.
Central Research Question: Can we achieve high-throughput, in-flight telemetry obfuscation on constrained legacy hardware while guaranteeing 100% exact numerical restoration for authorized cloud systems?
Notes: SPEAKER SCRIPT:
When cybersecurity engineers look at this problem, they usually suggest two standard tools: First: 'Just encrypt everything with AES or TLS.' But on a 15-year-old PLC running a 16-bit microcontroller, there is no AES-NI hardware accelerator. Software AES introduces huge latency spikes that break real-time Modbus scan cycles and drop packets.
Second: 'Why not use Differential Privacy and add Gaussian or Laplacian noise?' Because in industrial control systems, noise is irreversible! If you permanently distort boiler pressure or chemical concentrations, your cloud safety monitoring system triggers false alarms or misses real disasters.
This framed our core research question: Can we design a system that scrambles data in-flight with near-zero latency, while allowing authorized cloud receivers to reverse it with 100% exact numerical restoration?

## Slide 4
SYSTEM ARCHITECTURE
L-RAPID: Lightweight Reversible Data Perturbation
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 4 of 13
1. Legacy Edge PLC
• Input: Modbus registers FC1–FC4.
• Register Packing: Packs four 16-bit values into a single 64-bit integer.
• Keystream Generation: Derives 64-bit mask from shared secret synchronization.
• In-Flight Masking: Applies packed bitwise XOR: C = P ⊕ K.
• Micro-Benchmark: Executes in 0.15 µs (sub-microsecond latency).
2. Untrusted Wiretap Link
• Network Channel: Public Internet, 4G cellular, or Wi-Fi gateway.
• Adversary Interception: Attacker intercepts perturbed telemetry stream.
• Obfuscated Signal: Features exhibit uniform high-entropy distribution.
• Static Attacker: Detection accuracy collapses to 48.8%.
• Adaptive Attacker: Stuck at 49.9% (equivalent to a 50/50 coin toss).
3. Authorized Cloud Ingestion
• Secure Ingestion: Cloud shares synchronization state with the PLC.
• Self-Inversion: Re-applies XOR: P = C ⊕ K.
• Reversibility: 100.0% Exact bit-for-bit restoration (0 reconstruction error).
• Full Utility: Preserves raw 98.47% baseline intrusion detection.
• Zero Decryption Math: No complex matrix inversions or modular arithmetic.
Self-Inverting Mathematical Principle: Ciphertext = Plaintext ⊕ Key ⇒ Restored = (Plaintext ⊕ Key) ⊕ Key = Plaintext
Because bitwise XOR is an involution, restoration requires zero computational overhead and guarantees exact arithmetic fidelity for cloud analytics.
Notes: SPEAKER SCRIPT:
This brings us to our solution: L-RAPID (Lightweight Reversible And Privacy-Preserving IIoT Data-Perturbation).
Here is how the 3-tier architecture operates:
1. At the Edge PLC: We take the 4 Modbus telemetry registers, pack them into a single 64-bit integer, and bitwise XOR them with a pseudorandom keystream in just 0.15 microseconds.
2. On the Wire: Any wiretapping adversary only observes high-entropy scrambled numbers. Even if they intercept the traffic and retrain an intrusion detection model on it, their accuracy drops to 49.9%—the exact equivalent of flipping a coin.
3. At the Authorized Cloud: Because both sides share the secret synchronization seed, the cloud regenerates the exact same keystream and applies the self-inverting XOR operation again. The data is restored with 100% exact numerical match, preserving full utility for analytics.

## Slide 5
CORE ARCHITECTURE
Packed 64-Bit Word-Parallel Bit Manipulation
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 5 of 13
Multi-Register Bit Packing Mechanics
The Modbus Telemetry Structure: Modbus frames stream multiple contiguous 16-bit registers. In our design, four registers span exactly 64 bits.
Conventional Register-by-Register Masking (16-bit): • Requires 4 independent memory loads, 4 XOR calls, and 4 memory stores. • Measured per-packet latency: 1.48 µs.
Our Approach: Packed Word-Parallel Processing (64-bit): uint64_t packed = ((uint64_t)FC1 << 48) | ((uint64_t)FC2 << 32) | ((uint64_t)FC3 << 16) | ((uint64_t)FC4); packed_perturbed = packed ^ keystream_64;
Throughput Impact: • A single 64-bit CPU instruction perturbs all 4 registers simultaneously. • Latency drops to 0.15 µs (10× faster than 16-bit masking)!
Important Architectural Distinctions
1. Word Parallelism vs. Cryptographic Diffusion: • Why is packed XOR 10× faster? It exploits 64-bit word-level parallelism inside modern edge CPU registers. • Scientific Nuance: Bitwise XOR does NOT diffuse entropy across register boundaries. Each register is masked by its corresponding 16-bit block. • The speedup is purely architectural, which is the honest engineering claim.
2. Masking Domain vs. Key Space: • The 64-bit approach spans a packed 64-bit masking domain (2^64 states ≈ 1.84 × 10^19 combinations). • In this prototype, the keystream is generated deterministically from a shared PRNG seed (999). • In production, this domain is seeded by dynamic stream ciphers (ChaCha20 or ASCON-128a) paired with per-packet nonces.
Notes: SPEAKER SCRIPT:
Let's look at the core technical innovation: Packed 64-Bit Word-Parallel processing.
In a standard Modbus packet, multiple 16-bit registers are transmitted together. If you perturb registers one by one, the CPU has to execute 4 separate load, XOR, and store instructions. That takes 1.48 microseconds.
Instead, we bit-pack all 4 registers into a single 64-bit integer word using simple bit-shifts. Now, a modern 64-bit processor executes the entire perturbation across all 4 registers in a single CPU instruction! That slashed our per-packet latency by 10×—down to 0.15 microseconds.
I want to highlight an honest scientific distinction: this speedup comes from architectural word parallelism, not cryptographic diffusion, because plain bitwise XOR does not mix bits across register boundaries. Being precise about this distinction is what makes our research solid.

## Slide 6
DATASET & BASELINE ML
ToN_IoT Modbus Dataset & Baseline Evaluation
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 6 of 13
The ToN_IoT Modbus Benchmark
• Benchmark Origin: Modbus telemetry subset of the ToN_IoT dataset (Nour Moustafa, IEEE Dataport, 2019).
• Sample Size: 31,106 industrial telemetry records reflecting real network SCADA traffic.
• Balanced Distribution: 15,000 Normal (48.2%) vs. 16,106 Attack (51.8%) samples.
• 5 Attack Categories: Scanning, Backdoor, Injection, XSS, and Password attacks.
• Telemetry Features: Four standard Modbus Function Codes: - FC1: Read Input Register (Analog sensor telemetry) - FC2: Read Discrete Value (Binary sensor states) - FC3: Read Holding Register (Actuator/configuration settings) - FC4: Read Coil (Discrete actuator states)
• Precision: Natively represented as 16-bit unsigned integers (uint16, range 0–65,535).
Baseline Machine Learning Anomaly Detection
Model Configuration: Random Forest Classifier (100 estimators, class_weight='balanced', random_state=42). 80/20 stratified train/test split (24,884 train / 6,222 test samples).
Empirical Baseline Results on Raw Telemetry: • Binary Detection Accuracy: 98.47% • Weighted F1-Score: 0.9847 • Test Set Misclassifications: Only 16 False Positives and 79 False Negatives out of 6,222 samples.
Key Scientific Takeaway: Unperturbed Modbus registers exhibit an exploitable, highly discriminative structure. Attackers intercepting raw streams can easily identify system operations with 98.5% confidence. This directly confirms the critical need for in-transit obfuscation.
Notes: SPEAKER SCRIPT:
To rigorously test our pipeline, we evaluated it against the Modbus subset of the ToN_IoT dataset, comprising 31,106 samples covering 5 real attack categories like Injection, Backdoor, and Scanning.
The dataset records four 16-bit Modbus registers: FC1 to FC4. First, we trained a baseline Random Forest classifier on the raw, clean data using an 80/20 stratified split. The baseline achieved 98.47% accuracy and an F1-score of 0.9847, making only 95 errors out of over 6,200 test samples.
This proved an important prerequisite: raw industrial Modbus telemetry has a very strong, exploitable pattern. Without perturbation, any attacker tapping the wire can easily monitor the plant's operational state.

## Slide 7
SECURITY EVALUATION
Dual Threat Modeling: Static vs. Adaptive Adversary
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 7 of 13
Threat Model 1: Static Adversary (Distribution Shift)
• Attacker Profile: Deploys a pre-trained intrusion detection model trained on clean historical telemetry.
• Operational Mode: Intercepts perturbed telemetry in-flight and evaluates it directly without retraining.
• Detection Outcome: Classification accuracy plummets from 98.47% down to 48.8%.
• Skeptical Counter-Argument: Is this accuracy collapse simply an out-of-distribution (covariate shift) artifact?
Threat Model 2: Adaptive Adversary (Active Retraining)
• Attacker Profile: Strong adversary with access to intercepted perturbed traffic AND ground-truth labels.
• Operational Mode: Trains a fresh Random Forest classifier directly on the perturbed feature space (80% training split).
• Detection Outcome: Accuracy remains completely suppressed at 49.9% (pure coin-toss guessing)!
• Theoretical Meaning: Zero mutual information advantage over random chance (50% privacy ceiling).
Key Academic Finding: Because direct retraining on perturbed data fails to exceed 50% accuracy, we prove that the defense is NOT just a covariate shift artifact. L-RAPID fundamentally eliminates the discriminative correlation between features and attack labels.
Notes: SPEAKER SCRIPT:
Now let's examine our security evaluation. This was the most important scientific contribution of our paper.
In peer review, Reviewer 2 asked a tough question: 'If you train a classifier on clean data and test it on scrambled data, of course accuracy drops. Isn't that just a distribution shift?'
To answer this definitively, we evaluated two separate adversaries:
First, the Static Adversary: an attacker using a pre-trained model on clean data. Accuracy dropped to 48.8%.
Second, the Adaptive Adversary: we gave the attacker an 80% training set of intercepted perturbed traffic WITH ground-truth labels, and let them train a fresh Random Forest model directly on the perturbed data.
Look at the result: even with full retraining, the adaptive adversary achieved only 49.9% accuracy—the exact equivalent of flipping a coin! This conclusively proves that our perturbation doesn't just confuse a static model; it obliterates the mutual information between features and class labels.

## Slide 8
SECURITY EVALUATION
Empirical Validation: Triad Confusion Matrix Analysis
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 8 of 13
Figure 1: Triad Confusion Matrix Evaluation — (Left) Clean Baseline 98.47% utility, (Center) Adaptive Adversary collapsed to ~50% random guessing floor, (Right) Cloud Restoration recovering 100% exact baseline detection fidelity.
Notes: SPEAKER SCRIPT:
Slide 8 displays our empirical Triad Confusion Matrix evaluation across all 6,222 test samples.
Look at the progression from left to right:
On the left, the clean baseline separates normal traffic from attacks almost flawlessly (98.47% accuracy).
In the middle, under L-RAPID perturbation, the confusion matrix collapses into an even distribution across all quadrants—true positives and false positives are equal, proving that the adversary is guessing at random.
On the right, upon authorized cloud restoration, the confusion matrix is restored bit-for-bit to the baseline state.
This visual triad provides empirical proof that data utility is completely preserved for the defender while denied to the eavesdropper.

## Slide 9
BENCHMARK RESULTS
Computational Latency Benchmark: Sub-Microsecond Speed
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 9 of 13
Perturbation Scheme | Exact Reversibility | Static Adv. Acc. | Adaptive Adv. Acc. | Per-Packet Latency | Speedup vs. AES-CBC
Original Raw Baseline | — | 98.47% | 98.47% | — | —
Gaussian Noise (sigma=0.5) | 100.0% | 51.4% | 50.8% | 1.82 µs | 5.8× faster
Laplacian Noise (b=0.5) | 100.0% | 48.2% | 49.6% | 2.10 µs | 5.0× faster
XOR 16-bit (Register-Level) | 100.0% | 49.1% | 50.2% | 1.48 µs | 7.1× faster
XOR 64-bit (Packed Word - Ours) | 100.0% | 48.8% | 49.9% | 0.15 µs | 69.8× faster (~70×)
ChaCha20 (CSPRNG Stream Cipher) | 100.0% | 49.9% | 50.0% | 7.12 µs | 1.5× faster (49× slower than XOR-64)
AES-128-CBC (Standard Block Mode) | 100.0% | 50.0% | 49.7% | 10.54 µs | 1.0× (Baseline Reference)
Key Benchmark Conclusions:
1. Sub-Microsecond Speed: Packed 64-bit XOR executes in 0.15 µs per packet, roughly 70× faster than AES-CBC (10.54 µs) and 59× faster than AES-CTR (8.87 µs).
2. Exact Mathematical Restoration: 100.0% exact match reconstruction across all 31,106 samples with zero numerical distortion.
3. Role of ChaCha20: Measured at 7.12 µs—faster than software AES, but ~49× slower than packed XOR. Serves as our production dynamic key derivation engine.
Notes: SPEAKER SCRIPT:
Here is our complete computational latency benchmark. We benchmarked our pipeline against standard AES and ChaCha20 over 10 repetitions across all 31,106 packets.
Look at row 5: our packed 64-bit XOR achieved a per-packet latency of just 0.15 microseconds. That is 69.8 times faster—roughly 70 times lower latency—than standard AES-CBC at 10.54 microseconds.
Why does this matter for the guests in the audience? In a Modbus RTU network with sub-millisecond scan cycles, an algorithm taking 10 microseconds per packet consumes significant CPU cycles on a 16 MHz microcontroller. At 0.15 microseconds, L-RAPID introduces practically zero delay, running comfortably on legacy hardware.
Notice also that every method achieved 100% exact numerical restoration. No distortion, zero error.

## Slide 10
BIT-DEPTH ANALYSIS
Parametric K-Bit Sweep: Tuning Perturbation Intensity
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 10 of 13
How Many Bits Must We Scramble?
The Engineering Question: Each Modbus register is 16 bits. Can an edge device save energy by scrambling fewer bits, or is full 16-bit scrambling required?
Sweep across K in {1, 2, 3, 4, 6, 8, 10, 12, 14, 16}: • K = 1 to 8 bits: Upper register bits remain unperturbed. Adversarial detection accuracy stays high at ~98.1% (insufficient privacy). • K = 10 to 12 bits: Accuracy begins dropping sharply (down to 75.9% at K=12). • K = 14 to 16 bits: The privacy collapse! Attacker accuracy plummets to 52.6% at K=14 and 49.57% (~50%) at K=16.
Practical Takeaway for Engineers: K acts as a tunable privacy dial. To achieve complete immunity against an adaptive AI adversary, all 16 bits must be scrambled.
Notes: SPEAKER SCRIPT:
We also asked a practical engineering question: Do we really need to scramble all 16 bits of each register? What if a resource-constrained sensor only scrambles the lowest few bits?
To answer this, we conducted a parametric experiment, varying the bit-depth K across selected values from 1 to 16. Look at the plot on the right:
When K is between 1 and 8 bits, the attacker's accuracy barely moves—it stays around 98%. Why? Because the top 8 bits of the register still carry enough operational structure for the AI to classify attacks.
However, once we cross K = 12 bits, the accuracy drops sharply to 75%, and by K = 14 and 16 bits, it completely collapses to 49.57%—the random guessing ceiling.
This establishes a crucial rule for industrial practitioners: to withstand an adaptive AI attacker, you must scramble all 16 bits.

## Slide 11
INDUSTRIAL IMPACT
Real-World Deployment: Where Can This Be Applied Today?
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 11 of 13
1. Smart Water Treatment
• Deployment: Remote pump stations and chlorination tanks transmitting over 4G/cellular to regional SCADA.
• Threat Scenario: Eavesdroppers discover chemical dosing schedules and pump timing to launch physical attacks.
• Why DP Fails: Permanent noise on chlorine or tank levels triggers false emergency shutdowns.
• L-RAPID Benefit: RTUs scramble telemetry in 0.15 µs; the cloud restores exact decimal values with 100% utility.
2. Renewable Power Substation
• Deployment: Wind turbines and solar substations streaming grid frequency and voltage every 10–50 ms.
• Threat Scenario: Strict sub-millisecond latency budgets. Software AES causes buffer overflows and desync.
• L-RAPID Benefit: At 0.15 µs, introduces zero lag. Protects grid telemetry from nation-state reconnaissance without risking blackouts.
3. Factory Cloud Predictive AI
• Deployment: Manufacturing plants streaming spindle vibration and heat data to public cloud AI (AWS / Azure).
• Threat Scenario: Competitors wiretap telemetry to deduce proprietary recipes, yield rates, and production volumes.
• L-RAPID Benefit: Gateway scrambles data before cloud ingestion; only authorized engineers reverse telemetry for digital twins.
Notes: SPEAKER SCRIPT:
Now let's ground this in reality: where can an industrial plant deploy this tomorrow?
Example 1: In municipal water treatment. Remote water pump stations transmit chemical dosing data over cellular. If attackers intercept it, they learn vulnerabilities. Permanent noise cannot be used because chlorine levels must be exact. L-RAPID scrambles data on low-power RTUs in 0.15 microseconds, and the central plant reverses it with 100% accuracy.
Example 2: In renewable power grids. Wind turbine substations have strict sub-millisecond control loops. Software AES causes packet buffers to fill up and drop packets, risking grid desynchronization. L-RAPID runs 70 times faster, introducing zero lag.
Example 3: In outsourced cloud predictive maintenance. Factories streaming machinery telemetry to AWS or Azure can protect their proprietary manufacturing recipes and production volume from corporate espionage.

## Slide 12
CRYPTOGRAPHIC DEFENSE
Security Analysis & Production Roadmap
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 12 of 13
Kerckhoffs's Principle: Open Algorithm Security
Anticipated Question: 'If your paper publishes the exact algorithm, can't attackers reverse-engineer the Modbus registers?'
Answer: Security Relies on Key Secrecy, Not Obscurity: 1. Math of XOR: P = C ⊕ K. Knowing the formula is XOR gives the attacker ZERO bits of information about the secret keystream K. All plaintexts remain equally likely. 2. Brute-Force Immunity: A 64-bit packed word spans 2^64 ≈ 18.4 quintillion states per packet. A cluster testing 1 billion keys/sec would require >580 years to brute-force a single frame. 3. Defeating Known-Plaintext Attacks (KPA): In production, keystream derivation is dynamic per-packet. Knowing packet #1 gives zero help in decrypting packet #2.
Production Roadmap & Future Work
1. Dynamic Keystream Derivation: • Prototype: Static seed (999) used strictly for experimental reproducibility. • Production: Integration with modern stream ciphers (ChaCha20 or ASCON-128a) paired with a per-packet nonce counter for forward secrecy.
2. Hardware-in-the-Loop (HIL) Deployment: • Deploying firmware on physical Siemens S7-1200 and Schneider Electric Modbus PLCs. • Empirical power profiling and CPU jitter benchmarking in operational testbeds.
3. Expansion to Full Journal Paper: • Expanding our 2-page conference abstract into a 10-page Journal paper (Draft_Paper_RDP_Modbus.md) with formal mutual information leakage bounds.
Notes: SPEAKER SCRIPT:
An attentive reviewer might ask: 'If you publish your paper explaining that you pack 4 registers and use XOR, can't an attacker just reverse-engineer it?'
The answer lies in Kerckhoffs's Principle, the fundamental law of cybersecurity: a system must be secure even if everything about the algorithm is public, as long as the key is secret.
Knowing that we use XOR gives the attacker zero information about the secret keystream K. Furthermore, our 64-bit packed word expands the search space to 18.4 quintillion states, making brute force impossible.
In our prototype, we used seed 999 for reproducibility. In our production roadmap, we replace this seed with ChaCha20 or ASCON-128a paired with a per-packet nonce, ensuring that every single Modbus packet gets a unique, unrepeatable key. We are currently preparing the full 10-page journal paper with hardware PLC deployments.

## Slide 13
SUMMARY
Conclusion & Summary of Contributions
CyberMACS 2026 | L-RAPID: Lightweight Reversible IIoT Telemetry Perturbation (Paper #203)
Slide 13 of 13
Sub-Microsecond Speed
• 0.15 µs per-packet latency.
• ~70× faster than AES-CBC.
• 10× faster than 16-bit XOR via packed 64-bit word parallelism.
• Zero real-time lag on legacy PLCs.
Adaptive AI Defense
• Baseline ML: 98.47% accuracy.
• Static Attacker: Drops to 48.8%.
• Adaptive Attacker: Drops to 49.9% even with 80% retraining.
• Zero exploitable discriminative structure.
100% Exact Utility
• 100.0% Exact match restoration.
• 0 reconstruction error.
• Unlike Differential Privacy, no permanent signal distortion.
• Full fidelity for cloud analytics.
Thank You! Questions & Discussion
Supported by Erasmus Mundus CyberMACS (Project #101082683) and TÜBİTAK-1001 (Project #125E288). Kadir Has University, Istanbul, Türkiye | Email: rabbihasan.himel@stu.khas.edu.tr
Notes: SPEAKER SCRIPT:
To conclude, L-RAPID delivers three fundamental breakthroughs for legacy IIoT security:
1. Sub-microsecond speed: executing in 0.15 microseconds per packet, roughly 70 times faster than AES-CBC.
2. Resilient AI defense: suppressing both static and adaptive adversaries to ~50% random guessing.
3. 100% exact numerical utility: restoring full telemetry fidelity for authorized cloud controllers without the destructive distortion of Differential Privacy.
This work was supported by the European Union under Erasmus Mundus CyberMACS and by TÜBİTAK-1001.
Thank you very much for your time and attention. I would now be delighted to answer any questions from the committee and the audience!